MORE System Requirements

Allan Standard Deviation budget

| Error Source | Allan deviation @103 s |
| --- | --- |
| Propagation Media | Total: 10–14 |
| Plasma | 3×10–16 * |
| Troposphere | 10–14 *** |
| Ionosphere | <3×10–16 * |
| Ground System | Sub-total: 6.2×10–15 |
| Frequency Standard | 10–15 |
| Receiver Chain | 3×10–17 * |
| Transmitter Chain | 3×10–16 * |
| Thermal and mechanical deformation | 6×10–15 |
| Station Location | 1.2×10–15 |
| Earth Solid Tides | 4×10–16 * |
| Spacecraft | Sub-total: 8×10–15 |
| Uncertainty of the HGA motion about the spacecraft centre of mass | 4×10–16 * |
| DST | 2×10–15 |
| KaT | 10–15 |
| TWTA | 5×10–17 * |
| High-Gain Antenna assembly thermo-mechanical stability ** | 6.7×10–15 |
| Uncertainty of MPO angular rate | 10–15 |
| Total | 1.4×10–14 |

* Feasible

** The effect of the reflector and pointing mechanism needs to be assessed.

*** Assuming use of water vapour radiometer.

| RSE Requirement ID in this document | Requirement | Source of the requirement | Verification (TBC) | Requirement Document (TBC) |
| --- | --- | --- | --- | --- |
| 1. | The MPO – Ground Segment link shall provide RSE Doppler measurements with an overall end-to-end Allan Standard Deviation less than 1.5×10–14 @ 1000s | MORE, | Analysis / Design | MIRD, SRD |
| 2. | The RSE Doppler measurement shall be obtained by the combination of the measurements in three two-way links in Ka/Ka (up and down), X/X (up and down) and X/Ka bands (up and down). | MORE | Design | MIRD, SRD |
| 3. | The final residuals, after calibration for propagation media, shall be less than 10–14 @ 1000s | MORE | Analysis | MIRD, SRD, (not yet part of) SGICD |
| 4. | The overall contribution of the Ground Segment to the Allan Standard Deviation in the Ka/Ka link shall be less than 6.2×10–15 | RSE Error Analysis Study, UdR | Analysis | MIRD, not (yet) part of SGICD |
| 5. | The overall contribution of the Space Segment to the Allan Standard Deviation of the Ka/Ka link Doppler measurements shall be less than 8×10-15 @ 1000s | RSE Error Analysis Study, UdR (modified) | Test | MIRD, SRD, EID-B |
| 6. (*) | The residual contribution of ionosphere and plasma to the Allan Standard Deviation shall less than (after plasma cancellation) 5×10–16 (@ 1000s) for impact parameters larger than eight solar radii | MORE | Design | MORE Team |
| 7. | The contribution of residual tropospheric noise to the Allan Standard Deviation shall be less than 10–14 (for elevation angles larger than 15 degrees, after suitable calibration, e.g. with WVR) | MORE, Error analysis study | Test | MIRD, SGICD not (yet) part of SGICD |
| 8. (*) | The contribution of the frequency standard to the Allan Standard Deviation of the Ka/Ka link Doppler measurements shall be less than 1×10-15 (@ 1000s) | MORE | Test | MIRD |
| 9. | The contribution of the receiver chain to the Allan Standard Deviation of the Ka/Ka link Doppler measurements shall be less than 8×10–16 @ 1000s | MORE | Test | MIRD |
| 10. | The contribution of Transmitter Chain to the Allan Standard Deviation of the Ka/Ka link Doppler measurements shall be less than 5×10–16 @ 1000s | MORE, corrected to maximum value of Allan SD to be tested. | Test | MIRD |
| 11. | The contribution of the thermal and mechanical deformations of the ground antenna to the Allan Standard Deviation (all links) shall be less than 6 ×10–15 (@ 1000s), under favourable conditions (wind less than 2 m/s and internal antenna temperature gradients less than TBD) | HTHGA TDA | Analysis and tests (to be devised) | MIRD |
| 12. | The contribution of the Station Location to the Allan Standard Deviation shall be less than 1.2×10–15 (@ 1000s) or, equivalently, the location shall be provided with 5 cm error. | MORE | Analysis | MIRD |
| 13. | The residual contribution of the earth solid tides to the Allan Standard Deviation shall be less than 5×10–16 @ 1000s (tides to be modelled by MORE). | MORE | Analysis | MORE |
| 14. | The contribution of Deep Space Transponder to the Allan Standard Deviation shall be less than 6×10–15 in the X/X link and less than 1×10–14 in X/Ka link (@ 1000s) | DST TDA | Test | SRD |
| 15. | The contribution of MORE (Ka/Ka link) to the Allan Standard Deviation shall be less than 1×10–15 @ 1000s | MORE | Test | MORE performance specification (EID-B) |
| 16. | The contribution of the high power amplifiers in X and Ka bands to the Allan Standard Deviation shall be less than 0.5×10–16 @ 1000s | MORE | Test | SRD |
| 17. | The contribution of high gain antenna (support structure, pointing assembly and reflector assembly, waveguides dilatation and antenna motion effects) to the Allan Standard Deviation of the Ka/Ka link shall be less than 6.7×10–15 @ 1000s | HTHGA TDA | Analysis based on unit tests | SRD |
| 18. | The relation between the Allan Deviation of the Ka/Ka, X/X and X/Ka shall be less than: ; except when specified otherwise | Error Analysis Study | Analysis | MIRD, SRD,MORE |

## 1.1	Range Requirements

Table 3-2 Raging errors statistical characterization

| Type of Error | High Frequencies: AWGN (standard deviation two way) | Intermediate Frequencies: Pass, Orbit, Measurement interval | Lowest Frequency: Maximum one year drift |
| --- | --- | --- | --- |
| Two-way error magnitude | 30 cm (goal 20 cm) | 30 cm (goal 20 cm) | 50 cm (goal 15 cm) |

Requirement Table 1. Range Performance

| RSE Requirement ID in this document | Requirement | Source of the requirement | Verification (TBC) | Requirement Document (TBC) |
| --- | --- | --- | --- | --- |
| 19. | The MPO – Ground Segment link shall provide and RSE ranging signal with a measurement noise error less than 15 cm (1 sigma, one-way TBC) | MORE | Design and analysis and test (Long Loop on the Ground Station) | MIRD, SRD |
| 20. | The MPO-Ground Segment link shall provide and RSE ranging signal with an overall ranging measurement bias calibration error less than 0.4 ns (1 sigma, one-way) | MORE | Design and analysis and test | MIRD, SRD |
| 21. | The overall RSE ranging performance shall be provided by three two-way links: Ka/Ka band, X/X band and X/Ka, for Up/Down link respectively | MORE | Design | SRD/MIRD |
| 22. | The RSE X/Ka two-way ranging measurement noise error evaluated according to the jitter formula (see Ref. TBD) shall be less than 2 m (1 sigma) | MORE | Test | SRD |
| 23. | The RSE X/X two-way ranging measurement noise error evaluated according to the jitter formula (see Ref. TBD) shall be less than 80 cm (1 sigma) | MORE | Test | SRD |
| 24. | The RSE Ka/Ka two-way ranging measurement noise error evaluated according to the jitter formula (see Ref. TBD) shall be less than 18 cm (1 sigma) | RSE Error Analysis Study | Test | SRD |
| 25. | The RSE Ka/Ka end to end calibration error for two-way range shall be less then than 0.7 ns | MORE | Analysis |  |
| 26. | The RSE Ka/Ka two-way ranging measurement Ground Segment calibration error shall be less then than 0.2 ns (TBC) | MORE | Test and Analysis | SRDMIRD |
| 27. | The RSE Ka/Ka two-way ranging measurement Space Segment calibration error shall be less then than 0.5 ns | MORE | Test | SRD, MORE |
| 28. | The RSE X/X and X/Ka two-way ranging measurement end to end calibration error shall be less then than 2.5 ns (TBC) | MORE | Analysis | SRD |
| 29. | The RSE X/X and X/Ka two-way ranging measurement Ground Segment calibration error shall be less then than 1.5 ns (TBC) A relative accuracy of this order of magnitude might be achievable. | MORE | Test and Analysis | SRD, SGICD not (yet) in SGICD |
| 30. | The RSE X/X and X/Ka two-way ranging measurement Space Segment calibration error shall be less then than 1 ns (TBC) | MORE and DST TDA | Test | SRD |

## 1.2	Orbit

Requirement Table 2. Orbit for RSE

| RSE Requirement ID in this document | Requirement | Source of the requirement | Verification (TBC) | Requirement Document (TBC) |
| --- | --- | --- | --- | --- |
| 31. | The MPO Mercury orbit shall be as described in EIDA | BC System Studies and Mission Analysis | Design | MIRD |

## 1.3	Operations

### 1.3.1	Cruise operations

MORE is primarily operated once Mercury orbit is attained. The cruise phase will be used with four main goals:

- Instrument calibration and testing

- Ground system testing

- Superior conjunction experiment (SCE)

- Precise navigation measurements

.

Requirement Table 3 RSE operational requirements during cruise

| RSE Requirement ID in this document | Requirement | Source of the requirement | Verification (TBC) | Requirement Document (TBC) |
| --- | --- | --- | --- | --- |
| 32. | The cruise composite shall provide the necessary resources to the MORE and ISA instruments (power, thermal control, data rate, full RSE link via HGA, quiet vibration environment) during a suitable superior solar conjunction during cruise (with Solar Elongation Angle Range from 0.7 to 2 deg TBC) in order to perform the Solar Conjunction Experiment. | Error Analysis Study | Design, Operations Plan | SRD, MIRD |
| 33. | The cruise composite shall provide the necessary resources to ISA (power, thermal control, data rate) during a TBD long coasting phase of the cruise in order to perform its calibration. | ISA | Design, Operations Plan | SRD, MIRD |
| 34. | The cruise composite shall provide the necessary resources to MORE (power, thermal control, data rate, full RSE multifrequency link via HGA) during 8-16 Ground Station passes as soon as possible during the cruise phase in order to perform its calibration. GOAL TBC | MORE | Design, Operations Plan | SRD, MIRD |
| 35. | The cruise composite shall provide the necessary resources to MORE (power, thermal control) continuously during the cruise phase in order to age and stabilise the instrument group delay | MORE | Design, Operations Plan | SRD, MIRD, |

### 1.3.2	Operations at Mercury

Requirement Table 4. MPO Orbit Operational Requirements

| RSE Requirement ID in this document | Requirement | Source of the requirement | Verification (TBC) | Requirement Document (TBC) |
| --- | --- | --- | --- | --- |
| 36. | The MORE and ISA onboard instruments and the ground triple link receiver shall be operational and provide measurements simultaneously during the periods at which the MPO can be tracked at the Ground Station with enough accuracy (minimum elevation angle 15 oC TBC, minimum Sun-Earth-Probe angle of 0.7 deg | Error Analysis Study, MORE, ISA | Design and Analysis | SRD, MIRD, SGICD |
| 37. | There shall be at least one RSE (triple link, calibrated TBC) ranging measurement every 15 minutes in average (more frequent TBD during Superior Conjunction) | MORE | Design | SRD, MIRD, SGICD |
| 38. | There shall be continuous RSE (triple link) Doppler measurements during MPO visibility (minimum elevation angle 15 deg TBC, minimum Sun-Earth-Probe angle 0.7 deg) | MORE | Design or Operations Plan | SRD, EID-B, SGICD |
| 39. | There shall be a calibration of the ground station before every RSE ranging measurement (TBC) | MORE | Design | SRD, MIRD, SGICD not yet in SGICD |
| 40. | ISA shall be powered permanently in nominal conditions/mode during the MPO Mercury orbit phase, also when measurements are not being taken | ISA | Design | SRD |
| 41. | There shall be no wheel desaturation attitude manoeuvres during the periods of ISA and MORE measurement | Error Analysis Study | Design | SRD, MIRD, |
| 42. | There shall be MPO Centre of Mass calibration manouvres outside the RSE measurement periods. These manouvres shall be defined in TBD. The frequency and duration of this manouvres shall be TBD. (this is an ISA requirement. It is left for completeness of information) | System Definition Studies | Design | SRD, MIRD |
| 43. | Ground range and range rate measurements, onboard acceleration measurements and HRC images for the libration experiment will be time tagged and synchronised with UTC with an error smaller than, respectively, 5 microseconds, 0.5 ms and 0.5 ms | MORE | Design, Testing | SRD, EID-B, |

## 1.4	Pointing

Requirement Table 5. Pointing Requirements

| RSE Requirement ID in this document | Requirement | Source of the requirement | Verification (TBC) | Requirement Document (TBC) |
| --- | --- | --- | --- | --- |
| 44. | The processed High Resolution Camera images shall have a resolution of 19 m at an altitude of 1500 km. NOTE: If the resolution of the processed images is 1 pixel (TBC), then this requirement is applicable to the pixel size of the HRC directly. | Error Analysis Study, SIMBIO-SYS | Analysis and Design | ? |
| 45. | The thermomechanical distorsion of the structure between the HRC and the Star Tracker shall be less than 1.5” RMS (GOAL: 1” RMS) for any image pair interval. An image pair interval is a time interval 30 to 60 days centered in the aphelion or perihelion. | Definition Studies | Test | EID-B |
| 46. | The (Generalised) Relative Measurement Error between the two HRC Line of Sights of each image pair shall be less than 2.5” RMS (GOAL: 2” RMS). The time interval between two images of a pair is 30 to 60 days centered in the apohelium or perihelium. | Definition Studies | Test | EID-B |